## Slide 1
L3: Accelerator-Friendly Lossless Image Format for High-Resolution, High-Throughput
DNN Training
Jonghyun Bae Woohyeon Baek Tae Jun Ham Jae W. Lee
Seoul National University, Korea
Notes: Hello, everyone.
I’m Jonghyun Bae from Seoul National University in Korea.
This video briefly explain about our research L3, the accelerator friendly lossless image format.

## Slide 2: DNN Training Pipeline
Load 0
Decode 0
Compute 0
Ideal DNN training pipeline
Time
Process on CPU
Process on GPU
Process on CPU and/or GPU
Load 1
Decode 1
Compute 1
Load 2
Decode 2
Compute 2
Load 3
Decode 3
Compute 3
...
Ideal DNN training
  Hiding data preparation (Load + Decode) by Compute  GPU-bound
Notes: The training process of deep neural networks is usually pipelined with stages for data preparation on CPUs followed by gradient computation on accelerators like GPUs.
In an ideal pipeline, the end-to-end training throughput is eventually limited by the throughput of the accelerator or GPU-bound, not by that of data preparation.
In the past, the DNN training pipeline achieved a near-optimal throughput by utilizing datasets encoded with a lightweight, lossy image format like JPEG.

## Slide 3: DNN Training Pipeline with Data Stalls
Ideal DNN training
  Hiding data preparation (Load + Decode) by Compute  GPU-bound
DNN training with data stalls
  Data stall caused by Load or Decode  CPU-bound or I/O-bound
Time
Load 0
Decode 0
Compute 0
Process on CPU
Process on GPU
Process on CPU and/or GPU
Load 1
Compute 1
Load 2
Compute 2
Decode 1
Decode 2
Data stall
Data pipeline with data stalls
Notes: However,
as high-resolution, losslessly-encoded datasets become more popular for applications requiring high accuracy
a performance problem arises in the data preparation stage
due to low-throughput image loading on the storage, and image decoding on the CPU.

## Slide 4: DNN Training Pipeline with Data Stalls
Time
Load 0
Decode 0
Compute 0
Process on CPU
Process on GPU
Process on CPU and/or GPU
Load 1
Compute 1
Load 2
Compute 2
Decode 1
Decode 2
Data stall
Data pipeline with data stalls
Load and Decode execution normalized to the Compute time
Notes: The graph compares the Load and Decode time with the Compute time for two segmentation models, and one detection model.
As shown in the graph. the PNG, JP2, and lossless WebP which require a complex decoding process spend more time on Decode than Compute;
this implies that the DNN training pipeline is bottlenecked by Decode.
On the other hand,
the BMP has a longer Load time than Compute time,
because the uncompressed BMP data tends to be much larger than other compressed image formats.
Among those measured, the JPEG is the only one that is not bottlenecked in data preparation.
However, JPEG is a lossy image format that loses some information in the original data.

## Slide 5: Comparison of Lossless and Lossy Image Formats
Degradation of the test-set accuracy with the use of JPEG and WebP
Model (Metric) | Lossless | Lossy | 
 | PNG | JPEG (Acc. diff) | WebP (Acc. diff)
DDRNet23-slim (mIoU) | 0.729 | 0.693 (-0.036) | 0.689 (-0.04)
DeepLabv3+ (mIoU) | 0.801 | 0.801 (0) | 0.808 (+0.007)
MaskFormer (mIoU) | 0.685 | 0.669 (-0.016) | 0.651 (-0.034)
PointRend (mIoU) | 0.722 | 0.711 (-0.011) | 0.712 (-0.01)
EgoNet (PCK@0.1) | 0.323 | 0.300 (-0.023) | 0.305 (-0.018)
PointPillars (mAP) | 0.611 | 0.593 (-0.018) | 0.582 (-0.029)
YOLOv5 (mAP@50) | 0.633 | 0.605 (-0.028) | 0.614 (-0.019)
Notes: The table shows the impact of lossy image format on the test set accuracy of seven object detection and semantic segmentation models, which are often deployed for autonomous driving.
The use of the lossy image format results in degradation of the test set accuracy in all models except DeepLabv3+, compared to a case where the lossless PNG format is used for encoding.

## Slide 6: Design Goal
Maximizing decoding throughput by leveraging the GPU
Providing a good-enough compression ratio not to introduce a new bottleneck in the Load stage
Notes: Therefore, the design goal of new image format is to eliminate the data preparation bottleneck by maximizing decoding throughput by leveraging the GPU
while providing a good-enough compression ratio not to introduce a new bottleneck in the Load stage.

## Slide 7: Comparison of L3 Design to PNG and JPEG
 | Algorithm |  | Lossless? | GPU-support?
 | Filter | Compression |  | 
PNG | Five types (None, Sub, Up, Avg, Paeth) | Deflate | O | X
JPEG | DCT, Quantization | Run-length + Huffman coding | X | ⃤
L3 | Custom Paeth | Base-delta coding | O | O
Notes: Thus, we propose L3, a custom lightweight, lossless image format for high-resolution, high-throughput DNN training.
While PNG decoder is not parallelized on GPU, the decoding process of L3 is effectively parallelized on the accelerator, thus minimizing CPU intervention for data preparation during DNN training. Thus, L3 yields much faster decoding than the existing lossless image formats whose decoders are mostly running on the CPU.

## Slide 8: Throughput Comparison with Lossless Decoders
Normalized training throughput with lossless-encoded datasets
1.71x and 1.31x training throughput increment compared to PNG and WebP
Notes: L3 achieves a 1.71x and 1.31x higher end-to-end training throughput than PNG and lossless WebP, the most popular lossless image formats on NVIDIA A100 GPU.

## Slide 9
Thank You
Source code of L3 is available at
https://github.com/SNU-ARC/L3.git
Notes: In summary, L3 effectively eliminates data preparation bottlenecks in the DNN training pipeline.
L3 can be readily deployed on GPU without requiring any support for specialized hardware.
L3 can significantly reduce the end-to-end training time by providing higher throughput, higher accuracy, or both,
compared to the existing lossless and lossy image formats at equivalent test set accuracy.
If you want to use L3, please visit the github.
Thank you.